E-143 DST Production 
                             from 8mm Stacker to Silo
                             ========================

                                            M. Daoudi, 15-Jan-95


This note describes a new DST production scheme for the E-143 experiment. It
makes use of two newly available tools at SLAC, namely a batch queue system
and a tape staging system. This new procedure with the capability of processing
several files in parallel in batch represents a substantial gain in CPU compared
to the one used previously. Another advantage is the fact that the output DST
data are written directly on the Silo tapes. Up to ten raw data tapes can be
processed automatically in a single job.

To use it do the following:
1. Login to one of the morgan machines.
2. Pick an 8mm tape stacker and prepare a stack of input raw data tapes (up to 
   10 tapes). 
   Prepare an input file containing the names of raw tapes and the names of the
   corresponding Silo cartridges you intend to use for the output DST data.
3. Issue the command:
   $E143_COM/raw2dstsilo taplis.fil stacker
   For example:
   $E143_COM/raw2dstsilo tape.list 1 >& 101to107.log &
  
   Where tape.list is as follows:
raw101  qa0021
raw102  qa0022
raw105  qa0023
raw107  qa0024
   (The first column corresponds to the input 8mm tapes, the second to the 
   silo tapes.)

Note 1:  Please make sure that the input raw tapes are mounted on the stacker
-------  from bottom to top as listed in the input file, and that their names 
do not exceed six (6) characters.
Note 2:  It is recommended to redirect the log and error output to the same
-------  file (e.g., >& 101to107.log in the example above).

Note 3:  In order to facilitate book keeping, try to start your raw2dstsilo
-------  jobs from one the these directories:
/usr/local/e143/dst2/m1/   if you are using   morgan01
                    /m2/                            02
                    /m3/                            03

Monitoring your job:
====================
There are several ways to monitor the progress of your raw2dstsilo job:
0. Do nothing! Everything will be all right! You will be notified when your
   job is finished. In the mean time find another stacker and start another
   job with 10 more raw tapes.
1. Look at the bottom of the log file (trivial ...hmmm).
2. Each raw tape is staged to disk. To see what files you own on the staging
   space, issue the command:
   stageqry -u
   Type "man stageqry" for more details on the stageqry command.
   The symbolic links corresponding to the files your raw2dstsilo job has on
   the staging space reside in the directory:
   /usr/local/e143/dst2/links/
3. For a given raw tape several files are processed in parallel in batch. To
   see what DST jobs your raw2dstsilo has submitted to the batch queue system,
   issue the command:
   bjobs
   Type "man bjobs" for more details on this command. A user-friendly X-window
   interface exists, issue the command:
   xlsbatch &
   Type "man xlsbatch" or "man lsbatch" to learn more about the LSF batch queue
   system.
4. The log files as well as the hbook files for all the DST jobs are written
   in the directory:
   /usr/local/e143/dst2/dstlog/
5. At the end of each DST job you will receive a mail message (with a log) from
   the batch queue system. I believe this can be suppressed if it becomes too
   annoying.
6. At the end of your raw2dstsilo job all the staging space it was using will
   be cleared.

Be happy!